## Domestic Heat Pump Water Heater

Air Source Heat Pump » Domestic Heat Pump Water Heater

Features of Domestic Heat Pump Water Heater 
1. The domestic heat pump water heater features compact design with 100/150/200/320L water tank available for option.
2. The outer tank case can be SUS304# or coated steel.
3. The equipment presents automatic defrosting function.
4. The domestic heat pump water heater has hydrophilic-coated copper-tube as heat exchanger.
5. The heat pump water heater is convenient for operation, as its remote wire LED screen digital controller is installed indoors 
6. Other heat exchanging coils can be installed inside the tank for a third heat source such as solar system and boilers which are also available.

Specifications of Domestic Heat Pump Water Heater

| Model |  | KF80-A/100F | KF80-A/150F | KF120-A/100F | KF120-A/200F | KF120-A/320F |
| --- | --- | --- | --- | --- | --- | --- |
| Power | HP | 1 | 1 | 1.5 | 1.5 | 1.5 |
| Heating capacity | kW | 3.71 | 3.71 | 5.58 | 5.58 | 5.58 |
|  | BTU/h | 12659 | 12659 | 19039 | 19039 | 19039 |
| COP |  | 4.12 | 4.12 | 4.46 | 4.46 | 4.46 |
| Water tank capacity | L | 100 | 150 | 100 | 200 | 320 |
| Rated heated water output | L/h | 80 | 80 | 120 | 120 | 120 |
| Rated outlet water temp. | ℃ | 55 |
| Max outlet water temp | ℃ | 60 |
| Rated power input | kW | 0.9 | 0.9 | 1.25 | 1.25 | 1.25 |
| Rated current | A | 3.73 | 3.73 | 5.89 | 5.89 | 5.89 |
| Power supply | V/PH/Hz | 220V ~ /50Hz |
| Compressor | Type | Rotary |
|  | Number | 1 |
| Heat exchanger type |  | Copper coil pipe |
| Throttling device |  | Capillary |
| Fan | Type | Low noise high efficiency axial type |
|  | Discharging | Horizontal |
|  | Quantity | 1 |
|  | Power input/W | 20 | 20 | 20 | 20 | 20 |
|  | Speed/RPM | 830 | 830 | 830 | 830 | 830 |
| Ambient temperature | ℃ | (-10℃ ~43℃ ) |
| Refrigerant |  | R22/R417A |
| Noise in 1 meter distance | dB | ≤ 54dB(A) |
| Water pipe size |  | Rc3/4 |
| Cabinet |  | Steel with powder coated |
| Low pressure protection system |  | Yes |
| High pressure protection system |  | Yes |
| Water flow switch |  | No |
| Automatically defrost system |  | Yes |
| Product dimension | mm | 850×260×540 | 850×260×540 | 850×260×540 | 850×260×540 | 850×260×540 |
| Package dimension | mm | 930×370×620 | 930×370×620 | 930×370×620 | 930×370×620 | 930×370×620 |
| Product dimension(water tank) | mm | ￠ 470*1121 | ￠ 470*1592 | ￠ 470*1121 | ￠ 555*1333 | ￠ 555*1839 |
| Package dimension(water tank) | mm | 520*520*1170 | 520*520*1580 | 520*520*1170 | 640*620*1390 | 620*640*1890 |
| Net weigh | kg | 31 | 31 | 33 | 33 | 33 |
| Gross weight | kg | 34 | 34 | 38 | 38 | 38 |
| Net weight(water tank) | kg | 28 | 34 | 28 | 48 | 58 |
| Gross weight(water tank) | kg | 48 | 60 | 48 | 72 | 86 |
| Testing condition: Ambient temp.(DB/WB) = 20℃ / 15 ℃ , Inlet/outlet water temp. = 15℃ /55℃ |

Domestic heat pump water heater with coil pipe in water tank is designed in order to provide sanitary hot water for family usage. It can be used in villas and apartments as well. The water can be heated up to 55DecC, with efficiency saving of 75% higher than traditional electric water heater. The heat pump and water tank are connected by the refrigerant pipe. Often the heat pump main unit is installed in outdoor, adopting a compact design, with traditional air conditioner appearance. It is very easy to locate and install. The water tank can be installed indoor and outdoor application optionally. The water tank capacity ranges from 100L to 320L, meeting demands of different families.

We are a manufacturer of domestic heat pump water heater in China. In addition, we offer household heat pump water heater, commercial air source heat pump, solar water heater, solar collector and more.

Company Brief:  Heat Pump Supply is an experienced air source heat pump manufacturer, located in China. Our primary products include domestic heat pump water heater, commercial air source heat pump, solar water heater and solar collector. They are widely used for heating water in families, offices, apartments, schools, swimming pools, and sauna rooms. Their safety, efficiency, environmental friendliness, easy operation, and long service life has made them highly sought after by customers from as far and wide as the United States, England, France, Italy, Poland, Australia, and more.

http://www.heatpumpsupply.com